## Slide 1
MONDAY UPDATE · ETHYLENE-CRACKER OUTLET · COMPUTED PAIRS ONLY
Eight process gases share a complete 471-MOF comparison set
The panel is ready for an apples-to-apples MOF screen; coverage alone cannot choose among the gases.
Directly computed coverage
All eight gases share the same 471 MOFs (24.3% of 1,940)
Chart: 
| Methane | Ethane | Ethylene | Propane | Propylene | Isobutane | Isopentane | 2-Pentene
Computed MOFs | 471 | 471 | 471 | 471 | 471 | 471 | 471 | 471
Eight-gas target panel
CORE FEED / PRODUCT GROUP
Methane
Ethane → Ethylene
Propane → Propylene
C4 / C5 PROXIES
Isobutane
Isopentane
2-Pentene
3,768
computed pairs
471
common MOFs
FULL COMPUTED DATASET 16,628 pairs · 1,940 MOFs · 113 molecules · 300 K · linear K
NEXT
Select 12 MOFs → test gas identification, composition drift & product/feed ratios → reduce if performance holds
Notes: Conditioned outlet means an extractive, post-quench/sample-conditioned sidestream near 300 K—not a MOF placed directly in the raw furnace effluent. The C4/C5 targets are coverage-matched process-gas proxies, not universal claims about dominant cracker products.
[Sources]
- https://zenodo.org/records/16754752 (D-MOPH-25 deposited computed data; accessed 2026-08-30)
- https://doi.org/10.1088/2632-2153/ae0241 (dataset methods, units, 300 K, and active-learning inventory)
- https://www.epa.gov/sites/default/files/2015-03/documents/subpartx-tsd-petrochem.pdf (ethylene-process context)
- https://cache.industry.siemens.com/dl/files/563/109770563/att_995347/v1/PIAAP-00002-0118-Ethylene.pdf (conditioned extractive furnace-effluent analysis context)
[/Sources]